## Slide 1: Radio Part 1
Lesson 18

## Slide 2: What The Lesson Will Cover
Know how micro:bit radio chip works
Be aware of the role of channel numbers in radio transmissions
Program a micro:bit to send data through the radio hardware
Program a micro:bit to receive data through the radio hardware

## Slide 3: The micro:bit Radio
The micro:bit has an inbuilt radio chip that can transmit to and receive messages from other micro:bits
Messages can be text, images and data
To achieve this:
  The micro:bits have to be connected – this is managed through the radio chip and the radio code module
  Next, data needs to be sent – this is sent as a byte (8 bits), by turning the signal on and off
  Each bit in the byte represents a value and these values are interpreted and converted into text, images or another action
  For example the value 73 might represent the word ‘Hello’
Notes: Demonstrate the radio feature working, sending a message to all the micro:bits
Introduce the radio hardware

## Slide 4: The micro:bit Radio
Radio transmits or broadcasts, which means that anyone nearby with a micro:bit can receive the data
Addressing is used to send the data to a micro:bit or group of micro:bits without others seeing the data
Addressing uses channel numbers where the radio is ‘tuned’ to a specific channel between the range 0 to 100
The radio module allows you to set the channel using the code radio.config(channel=19)– this sets the radio to channel 19
The micro:bit still receives broadcasts but filters out the messages that do not match your specific channel number
If you don’t set a channel number your micro:bit will receive every broadcast from every micro:bit
Notes: Introduce addressing and channel numbers

## Slide 5: Basic Code Sender
Import the radio module import radio
Turn the radio hardware on radio.on()
Set the channel number radio.config(channel=10)
Send a transmission radio.send()
The radio.send() code can send data, such as text, images and triggers words
When a trigger word is received the receiver micro:bit is coded how to respond
Trigger words can also be used to control hardware on another micro:bit, for example, if it receives the word ‘music’ then it plays the Nyan tune
It is also possible to send messages – this is covered in the next lesson
Notes: Talk over the sender code before Learners attempt the activity tasks

## Slide 6: Basic Code Receiver
Import the radio module import radio
Turn the radio hardware on radio.on()
Set the channel number radio.config(channel=10)
Receive a transmission radio.receive()
To receive any messages the channel number must be set to the same number as the micro:bit broadcasting
Then use the code to check for incoming message on that channel
Code is then used to tell the micro:bit what to do with the message: display it, play a sound or turn a motor
Notes: Talk over the receiver code before Learners attempt the activity tasks

## Slide 7: Activity
You are now going to complete the activity task where you will send data to and from one micro:bit to another
You need to pair up with another student
Decide which student will be the sender and which will be the receiver
Decide which channel number you are going to use
The sender student completes ‘program one’
The receiver student completes ‘program two’
Notes: The teacher may want to decide the channel numbers beforehand to avoid Learners sending and receiving unwanted messages.